## Slide 1: Sodium-potassium alloy (NaK)
NaK containing 40% to 90% potassium by weight is liquid at room temperature.
It is highly reactive with water and is stored usually under hexane or other hydrocarbons, or under an inert gas. (N2 or Ar)
When stored in air, it forms a yellow potassium superoxide coating and may ignite. This superoxide reacts explosively with water and organics.
Sodium-potassium alloys are used as desiccants in drying solvents prior to distillation.
Quenching procedure (< 10 g):
Slowly add the dry toluene to the stirring NaK and make sure that NaK in toluene is less than 20 wt%
After 5-10 min of stirring, add dry EtOAc slowly to the stirring solution. Potassium will be quenched first after 1 h.
Slowly add isopropanol until no more bubbling is observed. (first step for LiAiH4, NaBH4, CaH2, NaH, LiH, Li, Na)
Repeat with methanol, and then repeat with water.
(The water-reactive agent may still react violently with water. So add in small aliquots)